## Slide 1
F# | 1.7
EFL | 12 mm
TTL | 13.5 mm
Max. field | 3.21 mm
Distortion | < 0.16%
MTF | = 0.4 @ 300 lp/mm
Strehl ratio | = 0.59 @ Max. field
Relative illumination | > 0.85
1. Is there a way to ‘fully record’ the process that leads to a good design?
2. Can we review and analyze historical optimization processes to obtain a better design than before?
What if we no longer remember how it was obtained?
Initial structure
A historical best design

## Slide 2: KABBALAH — infrastructure for quantitative analysis of the optical design process
Reconstruct the complete real optimization history, including all failed/unsaved/rolled-back branches
Automatically save lens data after every optimization run
Automatically organize the history into a tree structure
Merge across files/logs/sessions over time
Translate low-level operations into natural language and add structured annotations to key operations (run optimization/view MTF...); users can freely edit/add annotations
Visual HTML files make human–AI interaction more efficient
......

## Slide 3
Unsaved rolled-back// failed operation branch
Two different branches derived from the same state

## Slide 4
SAVED state
ERR.F >100
1< ERR.F <100
ERR.F <1
HUMAN operation
set and run optimization

## Slide 5
Lens data are stored in the ‘state library’ (except the blue SAV state, whose corresponding local files already exist by default)

## Slide 6: What can this be used for?
Case 1: Analyze the direct effect of different distortion-constraint strategies on lens thickness
Case 2: Review an unsuccessful optimization route, identify the key operation step, and obtain a better design
Case 3: Analyze the evolution of L3L4 in the optimization history and quantify the mechanism behind the glass-material swap

## Slide 7: Case 1: Effect of distortion-constraint strategy on lens thickness
1. During trajectory review, GPT identified a clear change in designer behavior
ST000006 (initial spherical structure of this route)
Convert all lens surfaces to Qcon aspheres
Reduce F# and run automatic optimization
. . .
From F3.4,ST000015 onward, freeze all variables except the last lens L6, and reduce the center-thickness constraint from 2.4 to 1.8

## Slide 8: Case 1: Effect of distortion-constraint strategy on lens thickness
Inspect ST000015: the last lens is extremely thick

## Slide 9: Case 1: Effect of distortion-constraint strategy on lens thickness
2. Compare the distortion-constraint strategies of two routes
 | Route 1(initial distortion=0.07) |  | Route 2(initial distortion=0.12) | 
F# | DST constraint | L6_CT/TTL | DST constraint | L6_CT/TTL
4 | <0.05 | 12.18% | <0.12 | 7.41%
3.8 | <0.03 | 13.55% | <0.11 | 7.52%
3.6 | <0.01 | 15.33% | <0.10 | 8.05%
3.4 | <0.008 | 16.85% | <0.09 | 8.62%
<3.4 | Manual thickness repair begins |  | Normal optimization | 
3.0 |  |  | <0.06 | 10.76%
1.7 |  |  | <0.005 | 7.41%
Route 1
Route 2
Problem: the initial states are different

## Slide 10: Case 1: Effect of distortion-constraint strategy on lens thickness
 | Route 1(initial distortion=0.07) |  | Control route(same initial structure) | 
F# | DST constraint | L6_CT/TTL | DST constraint | L6_CT/TTL
4 | <0.05 | 12.18% | <0.07 | 11.69%
3.8 | <0.03 | 13.55% | <0.07 | 12.39%
3.6 | <0.01 | 15.33% | <0.07 | 13.36%
3.4 | <0.008 | 16.85% | <0.06 | 14.12%
<3.4 | Manual thickness repair begins |  | Normal optimization | 
3.0 |  |  | <0.06 | 15.26%
2.4 |  |  | <0.06 | 15.76%
<2.4 |  |  | Manual thickness repair begins | 
Route 1
Control route
3. Actively design a controlled experiment

## Slide 11: Case 1: Effect of distortion-constraint strategy on lens thickness
step1: During review, GPTidentified a clear change in the designer’s operation logic, revealing that the last lens was rapidly thickening during optimization.
step2: Ask GPTto compare two historical optimization routes and identify different distortion-constraint strategies.
step3：Design a controlled-route experiment to test the idea and formulate a data-supported hypothesis that can later be supported/rejected/refined.
Control route
Route 2
Route 1
Hypothesis: Tightening the distortion constraint too early can cause the last lens to thicken prematurely if the structure already has this tendency.

## Slide 12: Case 2: Recover a forgotten optimization process and obtain a better design
Initial spherical structure
A historical best design
A ‘nearly successful’ route
F# | 1.7
EFL | 12 mm
TTL | 13.5 mm
Max. field | 3.21 mm
Distortion | < 0.16%
MTF | = 0.4 @ 300 lp/mm
Strehl ratio | = 0.59 @ Max. field
Relative illumination | > 0.85
F# | 1.7
EFL | 12 mm
TTL | 13.5 mm
Max. field | 3.21 mm
Distortion | < 2.5%
MTF | = 0.48 @ 300 lp/mm
Strehl ratio | = 0.72 @ Max. field
Relative illumination | > 0.95
STOP = 0.1
STOP = - 0.3

## Slide 13: Case 2: Recover a forgotten optimization process through trajectory review
Identify the key operation order: glass swap → convert sphere to Qcon → optimize
S7
↓
S9
↓
Before swap: S7 n=1.55, v=55.82; S9 n=1.68, v=19.24
After swap: S7 n=1.68, v=19.24; S9 n=1.55, v=55.82
After L1L2 lens merge: spherical structure

## Slide 14: Case 2: Recover a forgotten optimization process through trajectory review
F# | 1.7
EFL | 12 mm
TTL | 14 mm
Max. field | 3.21 mm
Distortion | < 0.2%
MTF | = 0.48 @ 300 lp/mm
Strehl ratio | = 0.74 @ Max. field
Relative illumination | > 0.89
Final successful route
STOP = 0.1
Change the operation order: convert sphere to Qcon → optimize → glass swap → optimize

## Slide 15: Case 3: Analyze the mechanism behind the glass swap
L3
L4
Final successful route
No swap
glass swap
F# | 1.7
EFL | 12 mm
TTL | 13.5 mm
Max. field | 3.21 mm
Distortion | < 6%
MTF | = 0.25 @ 300 lp/mm
Strehl ratio | = 0.48 @ Max. field
Relative illumination | > 0.6
A failed route
F# | 1.7
EFL | 12 mm
TTL | 14 mm
Max. field | 3.21 mm
Distortion | < 0.2%
MTF | = 0.48 @ 300 lp/mm
Strehl ratio | = 0.74 @ Max. field
Relative illumination | > 0.89

## Slide 16
after opening Qcon, F/4.0
same initial structure
F/3.2
F/3.2
after opening Qcon, F/4.0
same initial structure
No swap
Glass swap

## Slide 17
Final F/1.7
Final F/1.7
F/2.2
F/2.6
F/2.6
F/2.2
No swap
Glass swap

## Slide 19
No-swap optimization route

## Slide 20
Glass-swap optimization route

## Slide 21: Achromat-like shape is dominant
n=1.68, v=19.24
n=1.55, v=55.82
easy
hard
easy
A local achromat-like structure may provide greater “effective structural freedom.” More precisely, this does not increase the number of variables; rather, under global chromatic-aberration and field-curvature constraints, it allows the local group to access a broader set of Petzval–Chromat feasible combinations. The local group does not need to satisfy C=0 or P=0; it only needs to carry a non-zero task assigned by the system (P,C). When two lenses can generate opposing chromatic contribution internally, shape/power can be redistributed without immediately paying a large global chromatic-aberration penalty, thereby enlarging the feasible space of structural evolution.

## Slide 22: Achromat-like shape is dominant
n=1.68, v=19.24
n=1.55, v=55.82
With the original glass order , L3/L4 it is difficult for L3/L4 to simultaneously provide the required chromatic compensation and Petzval contribution. In the original combination, if we want to form a L3 (-) / L4 (+) local achromat-like pair,i.e.,
Because the original L3 uses a high-Abbe -number glass (V3=55.82),L4 uses a low-Abbe -number glass (V4=19.24),the required power relation is:
Under the thin-lens approximation,
L3 has a lower n, so such a large negative power produces a large negative Petzval contribution.In other words, chromatic neutrality and the required Petzval role are in strong conflict under this glass ordering .

## Slide 23: achromat-like shape is dominant
n=1.68, v=19.24
n=1.55, v=55.82
easy
hard
easy
No swap initially
Swap

## Slide 24: Achromat-like shape is dominant
n=1.68, v=19.24
n=1.55, v=55.82
L3
L4
L2
When L3/L4 cannot economically carry the local chromatic task , more of the compensation responsibility shifts to L2. A stronger negative L2 power makes the marginal ray leaving L2 more divergent; after propagating across the L2–L3 separation, this increases the L3/L4 ray height .
F/# decreases further, this structure is more likely to encounter a marginal-ray ray-trace problem; To restore a traceable state, additional downstream positive power is required, causing a larger Petzval / field-curvature penalty.
L2
L3
L4

## Slide 25: How can designer language be converted into a quantitative description?
i
j
What exactly is ‘achromat-like shape’?
How do we describe ‘finding a stable compensation path’?
For a lens group (i,j), define the P-Cself-compensation coefficient K：
For a lens group (i,j), this describes the strength of its internal P-C self-compensation. For ‘achromat-like shape’,K → 0.

## Slide 26: How can designer language be converted into a quantitative description?
For two adjacent state, define the P-C evolution direction angle:
This describes the P-C compensation-evolution direction of the group at the current state.
We can then calculate the N-state state P-C evolution-direction coherence:
This describes whether, over the most recent N-state state, the structure follows a stable P-C compensation trajectory.
S_t
S_t+1

## Slide 27: How can designer language be converted into a quantitative description?
 | self-compensation coefficient K | Directional coherence R | Structural state
A | Low | High | Internal P–C compensation is strong, with coherent recent evolution
B | High | High | Internal P–C compensation is weak, but recent evolution remains coherent
C | High | Low | Internal P–C compensation is weak, with dispersed or frequently changing recent evolution
D | Low | Low | Internal P–C compensation is strong, while local functional roles are being redistributed

## Slide 28
Glass-swap route: L3L4 group: K,R7
Internal P–C compensation is weak, but recent evolution remains coherent
Internal P–C compensation is strong, with coherent recent evolution
Internal P–C compensation is strong, while local functional roles are being redistributed

## Slide 29
No-swap route: L3L4 group: K,R7
Internal P–C compensation is weak, but recent evolution remains coherent
Internal P–C compensation is weak, with dispersed or frequently changing recent evolution
Internal P–C compensation is weak, with dispersed or frequently changing recent evolution

## Slide 30
Designer language | AIQuantitative description easier for AI to interpret
L3/L4resembles an achromat-like lens group | K_34 → 0
this lens pair has weak chromatic and field-curvature compensation capability | K_34 ↑
the group evolves in a consistent direction | similar , high R_N
the group evolution is highly dispersed | dispersed , low R_N
... | 
Designer language | AIQuantitative description easier for AI to interpret
L3/L4resembles an achromat-like lens group | K_34 → 0
this lens pair has weak chromatic and field-curvature compensation capability | K_34 ↑
the group evolves in a consistent direction | 
the group evolution is highly dispersed | 
... | 

## Slide 31: What did KABBALAH change?
How questions are discovered: designer experience summaries → questions emerging naturally from optimization history
How problems are analyzed: horizontal comparison of multiple structures → longitudinal comparison along optimization trajectories
How hypotheses are formulated/tested: wait for the next design → quantitative comparison of multiple historical routes and actively designed control experiments during review
How optical design is communicated with AI: mainly text descriptions → AI retrieves and quantifies information directly from real design history

## Slide 32
Four files, compressed size: 533KB
140,000-line log compilation time = 5s
Only 6 manually saved initial/final results